## Slide 1
Wireless Networking:
OFDM and Modulation
CS 655: Wireless and Mobile Computing
Parth H. Pathak

## Slide 2: 802.11 PHY and MAC
 | 802.11b | 802.11a | 802.11g | 802.11n | 802.11ac
Frequency | 2.4 GHz | 5 GHz | 2.4 GHz | 2.4/5 GHz | 5 GHz
Channel width | 20 MHz | 20 MHz | 20 MHz | 20/40 MHz | 20/40/80/160 MHz
PHY | DSSS/CCK | OFDM | OFDM, DSSS/CCK | OFDM | OFDM
MIMO & beamforming | No | No | No | Yes | Yes
Max. data rate | 11 Mbps | 54 Mbps | 54 Mbps | 600 Mbps | ~6933 Mbps
MAC:
CSMA/CA and wideband medium access
PHY-I:
OFDM and modulation
PHY-II:
MIMO and beamforming

## Slide 3: Wireless communication primer
Sine wave
  Frequency, amplitude and phase
0.5
1
1.5
2
Time (t)
Amplitude
0
-1
1
0
A = 1
f = 1 Hz
= 0
WiFi
f = 20 MHz

## Slide 4: Modulation
Use the RF signal to represent bits
Amplitude, frequency and/or phase can be modulated
Amplitude
Frequency
Phase

## Slide 5: Modulation
Time (t)
-1
1
0
0.5
-0.5
Bit 0
Bit 1
Time (t)
-1
1
0
0.5
-0.5
Bit 0
Bit 1
Amplitude
Modulation
Frequency
Modulation

## Slide 6: Phase modulation
Binary Phase Shift Keying
    Bit 1: phase , Bit 0: phase 0
  Differential BPSK
    Bit 0 : no change in phase compared to previous bit
    Bit 1 : phase changes by compared to previous bit
0
1
0
0
1
0
BPSK
Differential PSK

## Slide 7: Phase modulation
Polar representation of phase shift keying schemes
1
00
01
0
11
10
BPSK
Quadrature PSK (QPSK)

## Slide 8: QAM modulation schemes
Quadrature Amplitude and Phase Modulation (QAM)
  Modulates both phase and amplitude of the signal
Commonly used in wired and wireless communications
  Most current 802.11 standards utilize QAM of different orders
  Also used in Long Term Evolution (LTE) 4G cellular networks

## Slide 9: I/Q representation
Instantaneous state of a sine wave can be represented using polar coordinate system
Amplitude

## Slide 10: I/Q representation
The polar representation is referred as I/Q data representation
Amplitude
What is I/Q data? Tutorial: http://www.ni.com/tutorial/4805/en/

## Slide 11: I/Q example
Change of phase in the desired signal
Change of amplitude in the sine and cosine signals

## Slide 12: QAM schemes
00
4 QAM
4 symbols
Each symbol represents 2 bits
01
11
10
16 QAM
16 symbols
Each symbol represents 4 bits
I
Q
I
Q

## Slide 13: OFDM
Orthogonal Frequency Division Multiplexing
A PHY layer technique
  Commonly used in wireless networks including 802.11 WiFi networks, LTE etc.
Properties
  Central idea: divide a large channel in multiple smaller subchannels, transmit data by encoding on the subchannels
  Why? Robustness against multi-path fading

## Slide 14: OFDM vs FDM
  FDM
    Non-overlapping subchannels
    Wastage of bandwidth necessary to separate subchannels
  OFDM
    Overlapping but orthogonal subchannels
    Carefully chosen subchannels – at the peak of each subcarrier, all other subcarriers are zero

## Slide 15: OFDM subcarriers
Freq.
Amplitude
At the peak of each subcarrier, all other subcarriers are zero

## Slide 16: OFDM subcarriers
Freq.
Amplitude
At the peak of each subcarrier, all other subcarriers are zero

## Slide 18: OFDM
How to spread information over the subcarriers?
Serial to parallel
Bit stream
0 1 0 0 1 1
Parallel to serial
Subcarrier 1
Subcarrier 2
Subcarrier 3
Subcarrier n
o o o

## Slide 19: OFDM
Example with 8 subcarriers
0 1 0 0 1 1 0 1 1 0 0 1 0 1 0 1
Sub 1 | 0 | 1
Sub 2 | 1 | 0
Sub 3 | 0 | 0
Sub 4 | 0 | 1
Sub 5 | 1 | 0
Sub 6 | 1 | 1
Sub 7 | 0 | 0
Sub 8 | 1 | 1
Step 1: Serial to parallel

## Slide 20: OFDM
Step 2: Modulate bits on each subcarrier
Sub 1 | 0 | 1
Sub 2 | 1 | 0
Sub 3 | 0 | 0
Sub 4 | 0 | 1
Sub 5 | 1 | 0
Sub 6 | 1 | 1
Sub 7 | 0 | 0
Sub 8 | 1 | 1
0
1
BPSK

## Slide 21: OFDM
Step 2: Modulate bits on each subcarrier
Sub 1 | 0 | 1
Sub 2 | 1 | 0
Sub 3 | 0 | 0
Sub 4 | 0 | 1
Sub 5 | 1 | 0
Sub 6 | 1 | 1
Sub 7 | 0 | 0
Sub 8 | 1 | 1
0
1
BPSK
0
0

## Slide 22: OFDM
Step 3: Combine subcarriers using IFFT to generate one channel waveform
Sub 1 | 0 | 1
Sub 2 | 1 | 0
Sub 3 | 0 | 0
Sub 4 | 0 | 1
Sub 5 | 1 | 0
Sub 6 | 1 | 1
Sub 7 | 0 | 0
Sub 8 | 1 | 1
o o o
o o o
o o o
IFFT
Resultant OFDM signal

## Slide 23: Why OFDM?
Wireless signal propagation is complex
  Stationary and moving objects affect the received signal
Signal reaches the receiver over multiple paths
  Variations in the environment results in frequency-selective fading

## Slide 24: Why OFDM?
Frequency selective fading
  Some frequencies within the channel fade severely
  These frequencies are uncorrelated
Ideal channel
f
A
Reality
f
A
Deep faded frequencies
Is it the same as path loss and shadow fading?

## Slide 25: Why OFDM?
Frequency selective affects only some subcarriers in OFDM
  Lower bit error rate
Single carrier
f
A
Deep faded frequencies
f
A
OFDM

## Slide 26: OFDM Block Diagram
Error correction coding
Interleaving
(serial to parallel)
Subcarrier modulation
IFFT
FFT
Subcarrier demodulation
Parallel to serial
Error correction decoding
Transmitter
Receiver

## Slide 27: Parity checking
single bit parity:
detect single bit errors
two-dimensional bit parity:
detect and correct single bit errors
0
0
Any limitations of this method?

## Slide 28: Forward Error Correction (FEC)
Wireless channel is inherently error prone
  Bit errors are common
  Can significantly reduce the achievable data rate
FEC
  Receiver can detect (to some extent) which bits were corrupted and correct them
  Additional parity bits are added to the data bits
  Commonly used FEC in 802.11 – Convolution codes
Coding rate
  No. of data bits / (no. of data bits + no. of parity bits)
  Coding rate of 1/2 means 50% bits are additional parity bits for FEC
  Coding rate of 3/4 means 25% bits are additional parity bits for FEC

## Slide 29: OFDM in 802.11a PHY
Channel bandwidth – 20 MHz
Total number of OFDM subcarriers – 48
FEC applied first to the incoming data bits
  Resultant data+parity bits are input to interleaving

## Slide 30: OFDM Block Diagram
Error correction coding
Interleaving
(serial to parallel)
Subcarrier modulation
IFFT
FFT
Subcarrier demodulation
Parallel to serial
Error correction decoding
Transmitter
Receiver

## Slide 31: Interleaving
Process of mapping the incoming data bits to subcarriers
  In practice, serial to parallel interleaving is not round-robin
General rule
  Map the consecutive bits to subcarriers far away from each other
  Reduces the probability of consecutive bits being dropped due to fading in nearby subcarriers – improves FEC performance
0 1 0 0 1 1 0
f
A

## Slide 32: Modulation
802.11a supports following modulation schemes
Modulation | Bits per symbol
BPSK | 1
QPSK | 2
16-QAM | 4
64-QAM | 6

## Slide 33: Block Interleaving
802.11a example
  48 subcarriers
  Modulation chosen - 64 QAM (6 bits per symbol)
Interleaver buffer size = 48 x 6 = 288 bits
b1, b2, b3, … , b288
Subcarrier no.
c1
c48
b241 | b242
b193 | b194
b145 | b146
b97 | b98
b49 | b50
b1 | b2
c2
b288
b240
b192
b144
b96
b48
…
…
…
…
0, 1, 0, … , 1
More complex versions of block interleavers used

## Slide 34: Subcarrier Modulation
Subcarrier symbol
b1, b2, b3, … , b288
c1
c48
b241 | b242
b193 | b194
b145 | b146
b97 | b98
b49 | b50
b1 | b2
c2
b288
b240
b192
b144
b96
b48
…
…
…
…
0, 1, 0, … , 1

## Slide 35: IFFT
Combine subcarriers
b1, b2, b3, … , b288
c1
c48
b241 | b242
b193 | b194
b145 | b146
b97 | b98
b49 | b50
b1 | b2
c2
b288
b240
b192
b144
b96
b48
…
…
…
…
0, 1, 0, … , 1
IFFT
Resultant OFDM symbol
…

## Slide 36: 802.11a OFDM PHY
Modulation | Coding rate | Coded bits per subcarrier symbol | Coded bits per OFDM symbol | Data bits per OFDM symbol | Data rate (Mbps)
BPSK | 1/2 |  |  |  | 
BPSK | 3/4 |  |  |  | 
QPSK | 1/2 |  |  |  | 
QPSK | 3/4 |  |  |  | 
16-QAM | 1/2 |  |  |  | 
16-QAM | 3/4 |  |  |  | 
64-QAM | 2/3 |  |  |  | 
64-QAM | 3/4 |  |  |  | 

## Slide 37: 802.11a OFDM PHY
Modulation | Coding rate | Coded bits per subcarrier symbol | Coded bits per OFDM symbol | Data bits per OFDM symbol | Data rate (Mbps)
BPSK | 1/2 | 1 |  |  | 
BPSK | 3/4 | 1 |  |  | 
QPSK | 1/2 | 2 |  |  | 
QPSK | 3/4 | 2 |  |  | 
16-QAM | 1/2 | 4 |  |  | 
16-QAM | 3/4 | 4 |  |  | 
64-QAM | 2/3 | 6 |  |  | 
64-QAM | 3/4 | 6 |  |  | 

## Slide 38: 802.11a OFDM PHY
Modulation | Coding rate | Coded bits per subcarrier symbol | Coded bits per OFDM symbol | Data bits per OFDM symbol | Data rate (Mbps)
BPSK | 1/2 | 1 | 48 |  | 
BPSK | 3/4 | 1 | 48 |  | 
QPSK | 1/2 | 2 | 96 |  | 
QPSK | 3/4 | 2 | 96 |  | 
16-QAM | 1/2 | 4 | 192 |  | 
16-QAM | 3/4 | 4 | 192 |  | 
64-QAM | 2/3 | 6 | 288 |  | 
64-QAM | 3/4 | 6 | 288 |  | 

## Slide 39: 802.11a OFDM PHY
Modulation | Coding rate | Coded bits per subcarrier symbol | Coded bits per OFDM symbol | Data bits per OFDM symbol | Data rate (Mbps)
BPSK | 1/2 | 1 | 48 | 24 | 
BPSK | 3/4 | 1 | 48 | 36 | 
QPSK | 1/2 | 2 | 96 | 48 | 
QPSK | 3/4 | 2 | 96 | 72 | 
16-QAM | 1/2 | 4 | 192 | 96 | 
16-QAM | 3/4 | 4 | 192 | 144 | 
64-QAM | 2/3 | 6 | 288 | 192 | 
64-QAM | 3/4 | 6 | 288 | 216 | 

## Slide 40: 802.11a OFDM PHY
Modulation | Coding rate | Coded bits per subcarrier symbol | Coded bits per OFDM symbol | Data bits per OFDM symbol | Data rate (Mbps)
BPSK | 1/2 | 1 | 48 | 24 | 6
BPSK | 3/4 | 1 | 48 | 36 | 9
QPSK | 1/2 | 2 | 96 | 48 | 12
QPSK | 3/4 | 2 | 96 | 72 | 18
16-QAM | 1/2 | 4 | 192 | 96 | 24
16-QAM | 3/4 | 4 | 192 | 144 | 36
64-QAM | 2/3 | 6 | 288 | 192 | 48
64-QAM | 3/4 | 6 | 288 | 216 | 54

## Slide 41: OFDM Block Diagram
Error correction coding
Interleaving
(serial to parallel)
Subcarrier modulation
IFFT
FFT
Subcarrier demodulation
Parallel to serial
Error correction decoding
Transmitter
Receiver

## Slide 42: Demodulation
Received symbols depend on channel variations
  Multi-path – common reason behind amplitude and phase changes
Mathworks - digital modulation with Matlab http://www.mathworks.com/help/comm/ug/digital-modulation_ja_JP.html
Transmitter
Receiver
Inter-symbol interference

## Slide 43: Demodulation
Hard decision
  Calculate the distance to the constellation points, pick the one with the lowest distance
  Can be overly conservative
Receiver

## Slide 44: Demodulation
Soft decision
  For the received symbol, calculate its distance to the nearby constellation points
  Use the distance to associate a probability to the constellation point
  Combine the probabilities with FEC decoding to minimize errors
Receiver

## Slide 45: Bit to symbol mapping
Natural vs. gray mapping in 16 QAM
Gray mapping: adjacent constellation points only differ in 1 bit
  Reduces bit error compared to natural mapping where adjacent points can have multiple bits different from each
3 (0011)
2 (0010)
7 (0111)
6 (0110)
1 (0001)
0 (0000)
5 (0101)
4 (0100)
11(1011)
10(1010)
15(1111)
14(1110)
9 (1001)
8 (1000)
13(1101)
12(1100)
2 (0010)
6 (0110)
3(0011)
7(0111)
14(1110)
10(1010)
15(1111)
11(1011)
1(0001)
5(0101)
0(0000)
4(0100)
13(1101)
9(1001)
12(1100)
8 (1000)
Natural mapping
Gray mapping

## Slide 46: OFDM in 802.11n
802.11n uses 20 and 40 MHz channel widths
  Following data rates refer to 20 MHz channels
Modulation | Coding rate | Data rate (Mbps)
BPSK | 1/2 | 6.5
QPSK | 1/2 | 13
QPSK | 3/4 | 19.5
16-QAM | 1/2 | 26
16-QAM | 3/4 | 39
64-QAM | 2/3 | 52
64-QAM | 3/4 | 58.5
64-QAM | 5/6 | 65

## Slide 47: OFDM in 802.11ac
802.11ac uses wider channel widths
  20, 40, 80 and 160 MHz
  More subcarriers for OFDM
For higher data rates, 160 MHz channel width and 256 QAM modulation can be used
Channel width (MHz) | OFDM subcarriers
20 | 52
40 | 108
80 | 234
160 | 468