## Slide 1: معماری کامپیوتر پیشرفته
وحید حقیقت دوست
haghighatdoost@shahed.ac.ir
http://ref.shahed.ac.ir/haghighatdoost
دانشکده فنی و مهندسی
فصل سوم
Instruction-Level Parallelism and Its Exploitation
Multiple Issue and Static Scheduling

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 6th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019

## Slide 3
Chapter 3
Instruction-Level Parallelism and Its Exploitation
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 4: Multiple Issue and Static Scheduling
To achieve CPI < 1, need to complete multiple instructions per clock
Solutions:
  Statically scheduled superscalar processors
  VLIW (very long instruction word) processors
  Dynamically scheduled superscalar processors
با همه تلاشی که در مباحث گذشته انجام دادیم، توانستیم کاری کنیم که CPI به یک نزدیک شود.
میخواهیم ساز و کاری را مطالعه کنیم که ما را به CPI<1 برساند.
یعنی در هر کلاک بیش از یک Instruction اجرا شود.

## Slide 5: Multiple Issue
Notes: EPIC : Exclosively Parallel Instruction Computing
VLIW: very long instruction word

## Slide 6: VLIW Processors
Package multiple operations into one instruction
Example VLIW processor:
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Must be enough parallelism in code to fill the available slots
Notes: VLIW: very long instruction word

## Slide 7: VLIW (very long instruction word) Processors
Disadvantages:
  Statically finding parallelism
  Code size
  No hazard detection hardware
  Binary code compatibility
f10
Notes:   Binary code compatibility
  کدی که تولید شده اگر هر دستور را با 5 دستور کوتاه ایجاد میکند. چنانچه سخت افزار تغییر یابد و بتواند در هر دستور بزرگ 6 دستور کوچک را قرار دهد، دیگر این کد قابل استفاده نیست

## Slide 8: Dynamic Scheduling, Multiple Issue, and Speculation
Modern microarchitectures:
  Dynamic scheduling + multiple issue + speculation
Two approaches for Multiple Issue:
  Assign reservation stations and update pipeline control table in half clock cycles
    Only supports 2 instructions/clock
  Design logic to handle any possible dependencies between the instructions
Issue logic is the bottleneck in dynamically scheduled superscalars

## Slide 9: Overview of Design

## Slide 10: Multiple Issue
Examine all the dependencies among the instructions in the bundle
If dependencies exist in bundle, encode them in reservation stations
Also need multiple completion/commit
To simplify RS allocation:
  Limit the number of instructions of a given class that can be issued in a “bundle”, i.e. on FP, one integer, one load, one store

## Slide 11: Example
Loop:ld x2,0(x1) //x2=array element
addi x2,x2,1 //increment x2
sd x2,0(x1) //store result
addi x1,x1,8 //increment pointer
bne x2,x3,Loop //branch if not last

## Slide 12: Example (No Speculation)

## Slide 13: Example (Mutiple Issue with Speculation)