## Slide 1: معماری کامپیوتر پیشرفته
وحید حقیقت دوست
haghighatdoost@shahed.ac.ir
http://ref.shahed.ac.ir/haghighatdoost
دانشکده فنی و مهندسی
فصل دوم
Memory Hierarchy Design
Replacement Policy

## Slide 2: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 5th edition, John L. Hennessy,‎ David A. Patterson, MK pub., 2019

## Slide 3
Computer Architecture
A Quantitative Approach, Sixth Edition
Hohn L. Hennessy
David A. Patterson
Chapter 2
Memory Hierarchy Design

## Slide 4: Replacement Policy
Cache has finite size
  What do we do when it is full?
Analogy: desktop full?
  Move books to bookshelf to make room
  Same idea:
  Move blocks to next level of cache

## Slide 5: Replacement Policy
How do we choose victim?
  Verbs: Victimize, evict, replace, cast out
Many policies are possible
  FIFO (first-in-first-out), shows anomaly
  Check line reference list 4 3 2 1 4 3 5 4 3 2 1 5 for 3-way and 4-way set
  LRU (least recently used), pseudo-LRU
  LFU (least frequently used)
  NRU (not recently used)
  Random  Pseudo-random
  Optimal
بهترین گزینه برای اخراج گزینه ای است که دیرتر از سایر بلاکهای موجود، به آن دسترسی خواهیم داشت.
Notes: سیاست اپتیمال وجود ندارد
بهترین گزینه برای اخراج گزینه ای است که دیرتر از سایر بلاکهای موجود، به آن دسترسی خواهیم داشت.

## Slide 6: Least-Recently Used
For W=2, LRU is equivalent to NRU
  Single bit per set indicates LRU/NRU
  Set/clear on each access
For W>2, LRU is difficult/expensive
  Timestamps? How many bits?
    Must find min timestamp on each eviction
  Sorted list? Re-sort on every access?
Overhead: bits per block
  8way -> 3 bit

## Slide 7: LRU
Notes: وقتی میزان انجمنی زیاد میشود، پیچیدگی LRU زیاد میشود. این همه شمارنده و بحث جستجو و ... زمان میبرد

## Slide 8: Pseudo-LRU
Notes: به ازای n بلوک در یک ست، n-1 بیت لازم داریم.

## Slide 9: Pseudo-LRU
;
3
replace
then
11
if
;
2
replace
then
10
if
;
1
replace
then
01
if
;
0
replace
then
00
if
80486)
Intel
in
used
(
:
2
0
2
0
1
0
1
0
Line
b
b
Line
b
b
Line
b
b
Line
b
b
replace
LRU
Pseudo
=
=
=
=
-
-
Mux
1
0
2
1
0
b
b
b
number
Line

## Slide 10: Practical Pseudo-LRU
Rather than true LRU, use binary tree
Each node records which half is older/newer
Update nodes on each reference
Follow older pointers to find pseudo-LRU victim
0
0
1
0
1
1
1
J
F
C
B
X
Y
A
Z
Older
Newer

## Slide 11: Practical Pseudo-LRU In Action
J
F
C
B
X
Y
A
Z
J
Y
X
Z
B
C
F
A
011: PLRU Block B is here
110: MRU block is here

## Slide 12: Practical Pseudo-LRU
Each access: flip nodes along path to block
Eviction: follow LRU path
Overhead: (W-1)/W bits per block
0
0
1
0
1
1
1
J
F
C
B
X
Y
A
Z
011: PLRU Block B is here
110: MRU block is here
Older
Newer
Refs: J,Y,X,Z,B,C,F,A

## Slide 13: True LRU Shortcomings
Streaming data/scans: x0, x1, …, xn
  Effectively no temporal reuse
Thrashing: reuse distance > W
  Temporal reuse exists but LRU fails
For n>W no blocks remain after scan/thrash
  Incur many conflict misses after scan ends
Pseudo-LRU sometimes helps a little bit

## Slide 14: LIP (LRU Insertion Policy)
Is a simplified variant of protected LRU
  Qureshi et al. ISCA 2007
Insert new blocks into filter part
  Here Filter list of size 1, reuse list of size (W-1)
Do this adaptively: Use set dueling to decide LIP vs. LRU
  1 (or a few) set uses LIP vs. 1 that uses LRU
  Compare hit rate for sets
  Set policy for all other sets to match best set
Notes: دو تا نو آوری دارند
1- بلوک جدید را بذاریم ته صف
2- اینکه LIP باشد یا LRU تعدادی ست را بعنوان مرجع درنظر میگیریم. مثلاً 32 تا با LRU و 32 تا با LIP.
در لحظه میبینیم که Miss rate کدام کمتر است.

## Slide 15: Not Recently Used (NRU)
Keep NRU state in 1 bit/block
  Bit is set to 1 when installed (assume reuse)
  Bit is set to 0 when referenced (reuse observed)
  Evictions favor NRU=1 blocks
  If all blocks are NRU=0
    Eviction forces all blocks in set to NRU=1
    Picks one as victim (can be pseudo-random, or rotating, or fixed left-to-right)
Provides some scan and thrash resistance
  Relies on “randomizing” evictions rather than strict LRU order
Used by Intel Itanium, Sparc T2

## Slide 16: Least Frequently Used
Counter per block, incremented on reference
Evictions choose lowest count
  Logic not trivial (W2 comparison/sort)
Storage overhead
  1 bit per block  like NRU
  How many bits are helpful?
Notes: دخیل نکردن زمان در این الگوریتم، باعث میشود این الگوریتم یک الگوریتم نا عادلانه باشد